## Slide 1: Do Do This at Home In Control?
Bob Frankston
https://Frankston.com

## Slide 2: Goals and Constrains
Control, not “automation”
  Dynamic vs carefully planned
  IP vs wired logic
Learn by Doing
Consumer Electronics
  Designed for everyday use
  Users as participants
  Users as Designers
Not annoy my family
  At least, not more then needed
Two-Way signaling

## Slide 3
Don’t do This at Home

## Slide 4: Preface
The Jetsons is winning  Alexa
It’s not just about light but we learn from 0’s and 1’s

## Slide 5: In The Beginning there was X10
At least the beginning of the journey
1970’s – power line signaling
Simply Turn Things on/off
16 Devices, 16 Houses (A-P) => 256 Devices
Keyed on AC 60Hz powerline
One way signaling
Wild cards for all and for lights
Notes: My DTMF story in Bexley

## Slide 6: X10 Evolves
Computer interface (serial port)
  Could listen as well as transmit
Additional codes for querying
Smart Home and others improved technology
Motion detection and wireless
Challenges
  Unreliable signaling
  Slow signaling
  Limited Devices

## Slide 7: Initial software
Module on PC
  Operations queue
  Trigger and rules
    Rules => Groups!
  Serialization
Multithreaded
  Use of queues
  And database
Also explore programming paradigms

## Slide 9: Initial Control Program
Written in Visual Basic 6
Oriented to X-10 challenges and hacks
Database with scripting
Serialized actions and simple rules/triggers
Lessons
  Automated scripts have limited utility
Distinguished desired response vs reported state
Trying to tame complexity

## Slide 10: Chance to try language features
Dynamic object creation
Dynamic scripting in C# and VB and ..
Rule Engine
Database
  Now with LINQ!
Structure values for Action and State/Status
  (oops)
  Distinguish “intent” vs “state”

## Slide 11: Improving X10 / CEBus
Much smarter
A special “turn on” for each device
Automagical configuration
Macro Language
Structure Wiring
  Powerline, coax and radio signaling
TDS – Too Damn Smart

## Slide 12: Other fancy protocols
Protocols that embed their limits
  IEEE-1394 / Firewire
  Bluetooth (and now, Bluetooth Mesh)
  Zigbee, Z-Wave
  Thread? (So close but …)
Limitations
  Separate physical facilities and distance limits
  Impose policies
  Need separate relaying
  Presume scarcity

## Slide 13: Other Protocol
Lutron
  Proprietary
  Patented Feedback!
Universal Power Line – UPB
  Noble attempt
  Still exists but niche

## Slide 14: Smart Home Insteon
In the spirit of X10 but better
  Higher speed powerline
  Fixed end point addresses – 24 bit
Original business model – OEM
Protocol by hardware people
  Limited number of hops and echo required
  Manual-inspired linking protocol
  Buggy initial implementation with very slow work-around
Did a very deep dive and built lots of tools

## Slide 15: Embracing Insteon
Generalized the program
  Additional device type
Lots of complex support
  Didn’t realize how dumb protocol is
  Had to program around hardware-designed protocols
Deployed devices more widely
Limited scale and devices

## Slide 16: SmartThings
Gateway to
  Z-Wave
  Zigbee etc..
  And more
Also
  Apps and virtual devices
  IFTTT
  Alexa etc..

## Slide 17: SmartThings
Working around the rule engine
  Wrote Groovy to program around
  Support own http(s) protocols
  Used IOTDB to work around OAuth
Cloud First
Zigbee/Z-Wave
  Having to pair (and unpair) devices
  Lots of hex codes

## Slide 18: Coexisting
My system
  Controls On/Off
  Controls Brightness
  Color etc.. is “To Do”
Coexist wit native apps
  Control colors etc..
  Option to change only some parameters

## Slide 19: FiOS
Upgrading to 150mbps forced me to cleanup Wi-Fi
  Speed itself is not that important above threshold
Ubiquiti
  Managing access points
  Robust coverage
  Managing static addresses
FiOS
  Uses MOCA
  STBs can use IP … but not with my own DHCP Server!

## Slide 20: Embracing the Web
Web App V1
  TypeScript Visual Studio
  Presented floor map w/editing
  Turns out buttons are more useful
  Event driven
  Widgets …
(My) server side
  http(s) listener
  Act as a nexus for state reporting
  Provides floor maps and device info

## Slide 21: LIFX
IP!!
  Bulbs as the end point
  Local and Cloud protocols
  App
Features
  Discovered color temperature and more
  Up to 1100 lumens, BR30, IR etc.
  But not outdoor
Teething problems
  Onboarding issues
  DHCP Issues

## Slide 22: Resilience and NodeJS and npm
Direct control from WebApp!
  Removes dependency on main system
  CORS  Need shim running on multiple machines (NodeJS)
  Still report status to central module
  Central module is still an option
Improved programming skills w/Async
IIS dispatch
  Was C# /name
  Now IISNode

## Slide 23: Embracing NodeJS
Scripting  NodeJS
  Nightlights
  Keep-ons
Visual Studio Code and TypeScript
Plan to shift functions to NodeJS
  Mañana
Programming C# vs TypeScript
  Flexibility of objects
  Vs. Linc

## Slide 24: Services
IFTTT – scaling
Alexa
Google Home
Apple Homekit
DIY – HomeAssistant, OpenHab etc.

## Slide 25: Hubitat
Box vs. DIY Pi
SmartThings emulation
  Added “MakerAPI” for me!
  Support for Hue, Yeelights, Nanoleaf Etc.
Runs in my house
Shifting my devices (a pain with Z-Wave)

## Slide 26: More IP Devices
Discover on Aliexpress and elsewhere
  Sonoff – Alexa etc.
    But can be reflashed with effort
  小米 (米家) / Ewelink
  Shelly – simplest API
    Also designed for reflashing

## Slide 27: Supporting
My own interfaces
  Insteon
  Lifx (using cloud but have local code in Node)
  Shelly
Via Hubitat
  Nanoleaf
  Yeelights
  Hue
  Zigbee and Z-Wave
Native apps for full capabilities and on-boarding

## Slide 28: IP Support
Using Ubiquity Unifi
  Managing naming and finding devices
  Static Addresses when necessary
  VLAN for guests
  Port mapping and Dynamic DNS
Issues
  Fall-over isn’t working automatically
  Dyn DNS support limited
  No API (Exploring using Puppeteer)

## Slide 31: Managing the networking

## Slide 32: Lots of lessons and questions
Need a peer internet
  Network of networks is the wrong model
Haven’t fully addresses trust/security issues
  Inherently ambiguous
Rules (IFTTT etc.) don’t scale and cannot be consistent
Where is knowledge of scenes
How do you I say “I want to read.

## Slide 33: Beyond light
Entertainment and ambiance
  Music and smart speakers
  Video and TV and home theater and the old STB
Doorbells, cameras
HVAC: Nest and thermostats and Rethinking HVAC
Baby monitoring and all that
Stepford Families and smart homes and cities
Computing and Alexa and the Jetsons

## Slide 34: Need more APIs
To control more of the home capabilities
But learn by doing
Escaping silos …

## Slide 35: Notes
Native vs. normalized
What does on/off do?
Where is a scene known?
Rules vs. Groups
Npm
Nest Y:\photos\ByDate\2018x\201804\20180413\IMG_20180413_121034.jpg